Total Marks: 30	Duration: 120 Min
Instructions:
- Follow coding guidelines.
- Check for error conditions.
- Do not use functions like scanf, exit, perror etc.
- Use printf only in non-computing functions

1	What is the output of below snippet? Justify. / #include <stdio.h> / int main(void) / { / enum e1{c11, c12} en1; / enum e2{c21, c22} en2; / en1 = c11; / en2 = c22; / if(en1 < en2) { / printf(“SUCCESS\n”); / else / printf(“FAILURE\n”); / return 0; / }	2
2	Write a program to implement a basic calculator which does following arithmetic operations. / Addition / Subtraction / Division / Multiplication / The operation to be done and the values to be operated on should be given as a part of command line arguments. Function prototypes are as given below. / int *add(int *, int, …); / int *sub(int *, int, …); / int *disvi(int *, int, …); / int *mul(int *, int, …); / Function should return NULL in case of errors, otherwise return the address of the variable that holds the generated results. / Example : / Input : ./calc add 2 3 4 5 6 / Output : 20	6
3	Explain analysis phase of compilation process with a snippet generating error/warning at each stage of analysis phase.	3
4	How is it possible for a variable qualified as static within a function to retain the value between function calls? Explain.	2
5	What is the difference between strncpy and memcpy? Explain.	3
6	Write a macro to swap first 4 bits with last bits of a given 32 bit integer.	4
7	Consider a file which contains only letters/alphabets; Write a program to convert case of each letter/alphabet within same file.	3
8	Explain structure padding with example.	2
9	What will be the output of below code snippets? / int main() / { / char *arr_str[4]={"global", "edge", "software", "limited"}; / printf("arr_str[1] = %s\n", *(arr_str + 1)); / printf("arr_str = %s\n", **arr_str); / printf("arr_str + 1 = %s\n", arr_str + 1); / return 0; / }
10	WAP to reverse the sentence, return the string. For example the input string “global edge software limited”, should output “limited software edge global”. It should be generic and work for any input. Do not use any temporary buffer. / Prototype: char *rev_sentence(char *in_output);	5

*** End of Question Paper ***
Questions Traceability Matrix
Topics	Question #	Simple	Medium	Complex
enum	1	1
Pointers	2,5,9,10		2	2
Compilation phases	3		1
Storage class specifiers	4		1
Bitwise	6		1
File operations	7		1
Structures	8	1
Total	10	2	6	2

Questions Tracker
Question #	Status	Question #	Status
1	Reviewed	9	Reviewed
2	Reviewed	10	New
3	Reviewed
4	Reviewed
5	Reviewed
6	New
7	Reviewed
8	Reviewed